## Slide 1: Vetromeccanica - AUTEFA communication version V2 =15.01.20 = AUTEFA Control system components Alpla Bowling Green IBSS_V2)
Communication Vetro bottle turner PLC -> TLO PLC
Communication Vetro Line PLC -> Autefa Safety Control PLC for batch handling

## Slide 2: Component details Vetro bottle turner PLC -> AUTEFA TLO PLC
8 x TLO PLC
Siemens PLC 1500F
8 x TLO HMI
IPC 12“ for HMI
7 x 2 Bottle turner PLC
Lenze PLC 3200 C
7 x 2 HMI Camera
8 x 1
guide adjustment PLC
Siemens PLC 1500 (CPU1515)
7 x 2 HMI Turner
8 x 1 HMI Guide adjustment
Remark:
no bottle turners on TLO25

## Slide 3
TLO PLC
(Trayloaders Out) - Profinet Master
Profinet – I Device
Communication Vetro bottle turner PLC -> AUTEFA TLO PLC
Bottle Turner / Guide adjustments PLCs are connected to TLO local profinet network
Autefa PLC is Profinet master
Bottle turner / Guide adjustment PLCs are Profinet slaves
Bottle turner 1
PLC – Profinet Slave
Bottle turner 2
PLC – Profinet Slave
Signals from bottle turner PLC:
Counting value
No. of ejected bottles
operation mode
bottle jam
fault messages
performance bits (for OEE)
Guide adjustment
PLC – Profinet Slave
Remark:
no bottle turners on TLO25

## Slide 4
Communication Vetro bottle turner PLC -> AUTEFA TLO PLC
Signals from bottle turner PLC:
Counting value after turner
No. of ejected bottles
operation mode
bottle jam
fault messages
performance bits (for OEE)
changover process status
actual bottle type (feedback)
actual bottle colour (feedback)
actual speed override
Signals to bottle turner PLC:
changeover request
actual bottle type
actual bottle colour
reset counters

## Slide 5
Communication Vetro automatic guide adjustment PLC -> AUTEFA TLO PLC
Signals from guide adjustment PLC:
operation mode
fault messages
performance bits (for OEE)
changover process status
actual bottle type (feedback)
actual bottle colour (feedback)
Signals to guide adjustment PLC:
changeover request
actual bottle type
actual bottle colour

## Slide 6: Component details Vetro Line PLC -> AUTEFA SCO PLC
Siemens PLC 1500F
1 x Batch Control HMI
IPC 12“ for HMI
7 x Line PLC
Siemens PLC 1500
7 x HMI
TP 900 comfort (9‘‘)
1x SCO PLC
(Safety Control Outfeed Side)

## Slide 7
Vetro Line 1 PLC
Communication Vetro Line PLC -> AUTEFA SCO PLC
1x SCO PLC
(Safety Control Outfeed Side)
1 x Batch Handling HMI
Autefa TLO 21 PLC
Autefa TLO 22 PLC
Autefa TLO 23 PLC
Autefa TLO 24 PLC
Autefa TLO 25 PLC
Autefa TLO 27 PLC
Autefa TLO 28 PLC
Autefa TLO 26 PLC
Ethernet – Factory Network
Profinet IDevice – Factory Network
Vetro Line 2 PLC
Vetro Line 3 PLC
Vetro Line 4 PLC
Vetro Line 5 PLC
Vetro Line 6 PLC
Vetro Exportline 24 PLC

## Slide 8
Communication Vetro Line PLC -> AUTEFA SCO PLC
The data transfer between the AUTEFA PLCs and the VETRO-system will be implemented using standard Ethernet TCP / IP “socket” communication protocol.
Telegram length is always 100bytes due to requirements on VETRO side (Allen Bradley PLC, T_COMM blocks).
Please refer to document “Vetro_communication_vx.y.docx”

## Slide 9: History:
V1.0 initial draft January, 8th, 2020
V2.0 update after meeting at Autefa on January, 14th, 2020
V3.0 update including Vetro Exportline PLC, February 24th, 2020